## Slide 1: Visual Function is measured with character recognition testing (Visual Acuity testing)
The results of the Visual acuity testing does not yield consistent results for different characters sets (optotypes)
We would like to evaluate and quantify the ability to correctly identifies each of the characters used in visual acuity testing by:
  Humans – we will perform an adaptive multiple choice test for each optotype
  CNN – we would like to train a CNN to recognize characters in individual optotype sets or in the total opt

## Slide 2
Allen
Wright
Patti
Lea
NumPV
Landolt C
Tumbling E
HOTV
ETDRSsloan
SnellenSarrif
SnellenSloan
Optotype Libraries
NumLea
ET-x
ETL-Face
A
W
P
L
NPV
C
E
HOTV
ETDRS
SSa
SSl
NL
ETL-x
ETL-face
Folder
To come

## Slide 3
Variable Optical Distortion
Optotype displayed on monitor
Captured images
Sphere | Cyl | Axis | Spherical Equivalent | Difficulty
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0.5 | 1
0 | 1 | 45 | 0.5 | 1
0 | 1 | 90 | 0.5 | 1
0 | 1 | 135 | 0.5 | 1
0 | 3 | 0 | 1.5 | 2
0 | 3 | 45 | 1.5 | 2
0 | 3 | 90 | 1.5 | 2
0 | 3 | 135 | 1.5 | 2
0 | 6 | 0 | 3 | 5
0 | 6 | 45 | 3 | 5
0 | 6 | 90 | 3 | 5
0 | 6 | 135 | 3 | 5
2 | 0 | 0 | 2 | 3
2 | 1 | 0 | 2.5 | 4
2 | 1 | 45 | 2.5 | 4
2 | 1 | 90 | 2.5 | 4
2 | 1 | 135 | 2.5 | 4
2 | 3 | 0 | 3.5 | 6
2 | 3 | 45 | 3.5 | 6
2 | 3 | 90 | 3.5 | 6
2 | 3 | 135 | 3.5 | 6
2 | 6 | 0 | 5 | 9
2 | 6 | 45 | 5 | 9
2 | 6 | 90 | 5 | 9
2 | 6 | 135 | 5 | 9
4 | 0 | 0 | 4 | 7
4 | 1 | 0 | 4.5 | 8
4 | 1 | 45 | 4.5 | 8
4 | 1 | 90 | 4.5 | 8
4 | 1 | 135 | 4.5 | 8
4 | 3 | 0 | 5.5 | 10
4 | 3 | 45 | 5.5 | 10
4 | 3 | 90 | 5.5 | 10
4 | 3 | 135 | 5.5 | 10
4 | 6 | 0 | 7 | 13
4 | 6 | 45 | 7 | 13
4 | 6 | 90 | 7 | 13
4 | 6 | 135 | 7 | 13
6 | 0 | 0 | 6 | 11
6 | 1 | 0 | 6.5 | 12
6 | 1 | 45 | 6.5 | 12
6 | 1 | 90 | 6.5 | 12
6 | 1 | 135 | 6.5 | 12
6 | 3 | 0 | 7.5 | 14
6 | 3 | 45 | 7.5 | 14
6 | 3 | 90 | 7.5 | 14
6 | 3 | 135 | 7.5 | 14
6 | 6 | 0 | 9 | 15
6 | 6 | 45 | 9 | 15
6 | 6 | 90 | 9 | 15
6 | 6 | 135 | 9 | 15
Data Acquisition

## Slide 4: Goal
The algorithm will be trained on large characters with low optical distortion.
The algorithm will be tested on
  Large characters with high optical distortion
  Medium and small characters with low and high optical distortion
The algorithm must be forced to given an answer of what character it thinks is present (this may be based on a probability).
We would like to plot the probability profile for each optotypes

## Slide 5
Training Set
Testing set
File Name is
Correct Answer
Algorithm determines which character it “thinks” is displayed

## Slide 6
Algorithm determines which character it “thinks” is displayed
Training Set
Testing set
File Name is Correct Answer